## Slide 1: Review. Boolean Algebra.
Postulates, Theorems
Absorption, De Morgan’s theorems
Switching functions
Truth tables
Formulas, Canonical SOP, Minterms
Deriving Truth Tables and SOP
John F. Wakerly – Digital Design. 4th edition.
Chapter 4.

## Slide 2: Basic Postulates

## Slide 3: Theorems

## Slide 4: Theorems
Theorem 4 (Absorption)
(a) a + ab = a (b) a(a + b) = a
Examples:
(X + Y) + (X + Y)Z = X + Y [T4(a)]
AB'(AB' + B'C) = AB' [T4(b)]
Theorem 5
(a) a + a'b = a + b (b) a(a' + b) = ab
Examples:
B + AB'C'D = B + AC'D
(X + Y)((X + Y)' + Z) = (X + Y)Z

## Slide 5: Theorems
Theorem 6
(a) ab + ab' = a (b) (a + b)(a + b') = a
Examples:
ABC + AB'C = AC
(W' + X' + Y' + Z')(W' + X' + Y' + Z)(W' + X' + Y + Z')(W' + X' + Y + Z)
= (W' + X' + Y')(W' + X' + Y + Z')(W' + X' + Y + Z)
= (W' + X' + Y')(W' + X' + Y)
= (W' + X')

## Slide 6
Theorem 7
(a) ab + ab'c = ab + ac (b) (a + b)(a + b' + c) = (a + b)(a + c)
Examples:
wy' + wx'y + wxyz + wxz' = wy' + wx'y + wxy + wxz'
= wy' + wy + wxz'
= w + wxz'
= w
(x'y' + z)(w + x'y' + z') = (x'y' + z)(w + x'y')
Theorems

## Slide 7
Theorems
Theorem 8 (DeMorgan's Theorem)
(a) (a + b)' = a'b' (b) (ab)' = a' + b'
Generalized DeMorgan's Theorem
(a) (a + b + … z)' = a'b' … z' (b) (ab … z)' = a' + b' + … z'
Examples:
(a + bc)' = (a + (bc))'
= a'(bc)'
= a'(b' + c')
= a'b' + a'c'
Note: (a + bc)' ¹ a'b' + c'

## Slide 8: Algebraic Forms of Functions
Literal: A variable, complemented or uncomplemented.
Product term: A literal or literals ANDed together.
Sum term: A literal or literals ORed together.
SOP (Sum of Products):
ORing product terms
f(A, B, C) = ABC + A'C + B'C
POS (Product of Sums)
ANDing sum terms
f (A, B, C) = (A' + B' + C')(A + C')(B + C')

## Slide 9
Switching algebra: Boolean algebra with the set of elements K = {0, 1}
If there are n variables, we can define switching functions. Sixteen functions of two variables:
A switching function can be represented by a table as above, or by a switching expression as follows:
f0(A,B)= 0, f6(A,B) = AB' + A'B, f11(A,B) = AB + A'B + A'B' = A' + B, ...
Value of a function can be obtained by plugging in the values of all variables:
The value of f6 when A = 1 and B = 0 is: = 1 + 0 = 1.
Switching Functions

## Slide 10: Truth Tables
Show the value of a function for all possible input combinations.
Truth tables for OR, AND, and NOT:

## Slide 11: Truth tables for f(A,B,C) = AB + A'C + AC'

## Slide 12: Minterms. Canonical form.
A minterm is a product term in which all the variables appear exactly once either complemented or uncomplemented.
Minterms of three variables:
Canonical Sum of Products (canonical SOP):
  Represented as a sum of minterms only.
Example: f1(A,B,C) = A'BC' + ABC' + A'BC + ABC

## Slide 13: Deriving Truth Table and SOP
Canonical SOP
f1(A,B,C) = A'BC' + ABC' + A'BC + ABC
Compact form
f1(A,B,C) = m2 + m3 + m6 + m7
Minterm list form
f1(A,B,C) = ∑m (2,3,6,7)