## Slide 1: Circuit Analyze
Combinational or Sequential logic schematics show the circuit’s hardware implementation and give us some knowledge about the functions of the circuit.
The exact behavior of circuit sometimes cannot be described looking at the schematic.
On the schematic there is no way to show how the circuit behaves when the inputs are changed.
John F. Wakerly – Digital Design. 4th edition. Chapter 3.

## Slide 2: Timing Diagrams
To describe the circuit in more details and to show the output state depended on input dynamic changes we use Timing Diagrams.
At the beginning of experiment the value of A is logical “1”
After some time the value is changed to logical “0”
The circuit implementation logic has positive logic when:
  Logical “1” is represented as high voltage or as high level signal.
  Logical “0” is represented as low voltage or as low level signal.
The abscissa shows the time progress
The ordinate shows the signal level (voltage).

## Slide 3: Timing Diagram of two variables - A and B.
At the beginning of experiment the value of A=1, the value of B=0
After some time the values are changed A = 0, B=1
The axes are not shown. It is up to necessity to show them or not.

## Slide 4: Timing diagram of some clock by name C1 or Clock 1
Clock is a periodic signal.
Clock usually hasn’t beginning or end. It exists all the time while power is on and is used for synchronization of circuits.
For the period when the signal has high level sometime we say “The signal exists” or “There is a signal”.
For the period when the signal has low level we say “There is no signal” or “No signal”.
Usually the “Signal” and “No signal” times are equal and each takes the half of a clock period.

## Slide 5: Ideal Signal
Ideal signals have rectangular form.
The edges are vertical so the signal doesn’t spend time for changes from 1 to 0 and vice versa.

## Slide 6: Real Signal
The real signals haven’t vertical edges because of parasitic capacitance and resistance.
They have edges changed by natural logarithm exponent laws and sometime are not look like to signal forms we use in our timing diagrams.
In digital logic circuits we use another form of real signals which corresponds to requirements of digital logic development and also is possible to implement on real electronics.

## Slide 7: Real Signal form and properties for using in digital design
A real changing point of signal is the level of signal when the next circuit feels the change of signal on its input.

## Slide 8: Digital Signals in basic gates
The behavior of signal passing the NOT gate

## Slide 9: It’s comfortable to use rectangular signals
The rising and the falling times as well as the propagation delay time we we’ll use upon necessity when they become important for the circuit design process.
Usually this happens when we have a real gates on real chips and there is initial design requirement to take in account the real chip timing parameters.
We can suppose that when the signal is really changed somewhere between beginning or end of real rising edge then that point is the vertical rising edge of virtual signal.
This assumption makes our signals rectangular
However the propagation time we have to take in account in the next several examples to see how the signals pass through other gates.

## Slide 10: Delay on And gate
The propagation delay time is smaller than the signal itself
So we have delay
However we have correct delayed signals at the end of the circuit.

## Slide 11: Delay on OR gate
The propagation delay time is smaller than the signal itself
So we have delay
However in this case also we have correct delayed signals at the end of the circuit.

## Slide 12: Signal Race
Signal racing is the condition when two or more signals change almost simultaneously.
They can cause glitches or spikes in the output signal.
Racing caused by edges’ rising and falling time difference of different gates
To eliminate glitches we can use one of synchronization methods called Strobe (timing or clock pulse) – taking the value of signal (variable) when it’s correct for sure.

## Slide 13: Signal Racing caused by delay
The below circuit does a simple A AND B function however B is passed through the “n” gates and the final delay of gates is bigger than the signal length.
Here we have another type of racing caused by additional circuits delay of one of signals.