## Slide 1: Flip-flops
Inputs are logically disconnected from the output in time.
Therefore, any unpredicted changes in the input signals cannot affect the state of the final outputs.
The output accepts the value of input only once at defined time.

## Slide 2: The Edge-Triggered RS Flip-flop

## Slide 3: The Edge-Triggered RS Flip-flop
There is still one problem left to solve:
the possible race condition which may occur if both the S and R inputs are at logic 1 when CLK falls from logic 1 to logic 0.

## Slide 4: The JK Flip-flop (Jack Kilby)
Prevent any possibility of a "race" condition occurring when both the S and R inputs are at logic 1 when the CLK input falls from logic 1 to logic 0
At the same time, we still want the flip-flop to be able to change state on each falling edge of the CLK input, if the input logic signals call for this.
Therefore, the S or R input to be disabled depends on the current state of the slave latch outputs.
CLK | J | K | Q | Qn
0,1,0>1 | X | X | Q | Q
1>0 | 0 | 1 | Q | 0
1>0 | 1 | 0 | Q | 1
1>0 | 1 | 1 | Q | Q’

## Slide 5: The JK Flip-flop

## Slide 6: JK Flip Flop working in Toggle mode. Frequency or Clock Divider.