## Slide 1: Creating a Single Datapath
Now that we have examined the datapath components needed for the individual instruction classes, we can combine them into a single datapath.
This simplest datapath will attempt to execute all instructions in one clock cycle
This means that no datapath resource can be used more than once per instruction, so any element needed more than once must be duplicated.
We therefore need a memory for instructions separate from one for data.

## Slide 2: CPU Clocking (1/2)
For each instruction, how do we control the flow of information though the datapath?
Single Cycle CPU: All stages of an instruction completed within one long clock cycle
  Clock cycle sufficiently long to allow each instruction to complete all stages without interruption within one cycle
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Reg.
Write

## Slide 3: Duplication and Sharing
Although some of the functional units will need to be duplicated, many of the elements can be shared by different instruction flows.
To share a datapath element between two different instruction classes, we may need to allow multiple connections to the input of an element, using a multiplexor and control signal to select among the multiple inputs.

## Slide 4: The Datapath for Memory and R-type instructions
We have to combine specific parts of datapath for different instructions to create a general one.
Let’s first look at the datapath elements which are familiar for us and then to the strange elements appeared on this picture.
  Register file, ALU, Memory, Sign Extension unit – we know these.
  What are the Multiplexers – (Mux) ? Why we need them ?

## Slide 5: What are the Multiplexers ?
When 2 or more outputs we need to connect with one input then we cannot do it simply connecting the wires each to other
  We need a special device called Multiplexer
Mux has a control input and data inputs..
Depended on the Control input value (true or false) only one of the data inputs of Mux passes to the output while the other input is blocked.

## Slide 6: The Differences of Memory and R-type instructions
The operations of arithmetic-logical (or R-type) instructions and the memory instructions datapath are quite similar.
The key differences are the following:
  The arithmetic-logical instructions use the ALU, with the inputs coming from the two registers.
  The memory instructions can also use the ALU to do the address calculation, although the second input is the sign extended 16-bit offset field from the instruction.
Another difference:
  The value stored into a destination register comes from the ALU (for an R-type instruction) or the memory (for a load).

## Slide 7: Multiplexer’s usage
To create a datapath with only a single register file and a single ALU, we must support two different sources for the second ALU input, as well as two different sources for the data stored into the register file.
Thus, one multiplexor is placed at the ALU input and another at the write data input to the register file.

## Slide 8: Single Datapath
Now we can combine all the pieces to make a simple datapath for the MIPS architecture by adding
  the datapath for instruction fetch
  the datapath from R-type and memory instructions
  and the datapath for branches
An additional multiplexor is required to select either the sequentially following instruction address (PC + 4) or the branch target address to be written into the PC.
Now The branch instruction uses the main ALU for comparison of the register operands
So we must keep the adder for computing the branch target address.

## Slide 9: Single Datapath
2
1
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24