## Slide 1: Generic Steps of Datapath
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Register
Write
PC
Notes: missing: multiplexors or “data selectors” – where should they be in this picture and why?
also missing – opcode for control of what operations to perform
state elements vs combinational ones – combinational given the same input will always produce the same output – out depends only on the current input

## Slide 2: Datapath Walkthroughs (1/3)
add $r3,$r1,$r2 # r3 = r1+r2
  Stage 1: fetch this instruction, increment PC
  Stage 2: decode to determine it is an add, then read registers $r1 and $r2
  Stage 3: add the two values retrieved in Stage 2
  Stage 4: idle (nothing to write to memory)
  Stage 5: write result of Stage 3 into register $r3

## Slide 3: Example: add Instruction
instruction
memory
+4
registers
ALU
Data
memory
imm
2
1
3
add r3, r1, r2
reg[1]+ reg[2]
reg[2]
reg[1]
PC

## Slide 4: Datapath Walkthroughs (2/3)
slti $r3,$r1,17 # if (r1 <17 )r3 = 1 else r3 = 0
  Stage 1: fetch this instruction, increment PC
  Stage 2: decode to determine it is an slti, then read register $r1
  Stage 3: compare value retrieved in Stage 2 with the integer 17
  Stage 4: idle
  Stage 5: write the result of Stage 3 (1 if reg source was less than signed immediate, 0 otherwise) into register $r3

## Slide 5: Example: slti Instruction
instruction
memory
+4
registers
ALU
Data
memory
imm
3
1
x
slti r3, r1, 17
reg[1] <17?
17
reg[1]
PC

## Slide 6: Datapath Walkthroughs (3/3)
sw $r3,17($r1) # Mem[r1+17]=r3
  Stage 1: fetch this instruction, increment PC
  Stage 2: decode to determine it is a sw, then read registers $r1 and $r3
  Stage 3: add 17 to value in register $r1 (retrieved in Stage 2) to compute address
  Stage 4: write value in register $r3 (retrieved in Stage 2) into memory address computed in Stage 3
  Stage 5: idle (nothing to write into a register)

## Slide 7: Example: sw Instruction
instruction
memory
+4
registers
ALU
Data
memory
imm
3
1
x
SW r3, 17(r1)
reg[1] +17
17
reg[1]
MEM[r1+17]<=r3
reg[3]
PC

## Slide 8: Why Five Stages? (1/2)
Could we have a different number of stages?
  Yes, and other architectures do
So why does MIPS have five if instructions tend to idle for at least one stage?
  Five stages are the union of all the operations needed by all the instructions.
  One instruction uses all five stages: the load

## Slide 9: Why Five Stages? (2/2)
lw $r3,17($r1) # r3=Mem[r1+17]
  Stage 1: fetch this instruction, increment PC
  Stage 2: decode to determine it is a lw, then read register $r1
  Stage 3: add 17 to value in register $r1 (retrieved in Stage 2)
  Stage 4: read value from memory address computed in Stage 3
  Stage 5: write value read in Stage 4 into register $r3

## Slide 10: Example: lw Instruction
ALU
instruction
memory
+4
registers
Data
memory
imm
3
1
x
LW r3, 17(r1)
reg[1] +17
17
reg[1]
MEM[r1+17]
PC

## Slide 11: Peer Instruction Multiplexer usage
How many places in this diagram will need a multiplexor to select one from multiple inputs?
a) 0 b) 1 c) 2 d) 3 e) 4 or more

## Slide 12: Peer Instruction Multiplexer usage
How many places in this diagram will need a multiplexor to select one from multiple inputs
a) 0 b) 1 c) 2 d) 3 e) 4 or more

## Slide 13: Datapath and Control
Datapath based on data transfers required to perform instructions
Controller causes the right transfers to happen
PC
instruction
memory
+4
rt
rs
rd
registers
Data
memory
imm
ALU
Controller
opcode, funct

## Slide 14: Why a Single-Cycle Implementation Is Not Used Today
Although the single-cycle design will work correctly, it would not be used in modern designs because it is inefficient.
The clock cycle must have the same length for every instruction in this single-cycle design.
The clock cycle is determined by the longest possible path in the processor. This path is almost certainly a load instruction, which uses five functional units in series:
  the instruction memory,
  the register file,
  the ALU,
  the data memory,
  the register file.
The overall performance of a single-cycle implementation is likely to be poor, since the clock cycle is too long.

## Slide 15: CPU Clocking (2/2)
Alternative multiple-cycle CPU: only one stage of instruction per clock cycle
  Clock is made as long as the slowest stage
  Several significant advantages over single cycle execution: Unused stages in a particular instruction can be skipped OR instructions can be pipelined (overlapped)
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Register
Write

## Slide 16: A Multicycle implementation
Allows a functional unit to be used more than once per instruction, as long as it is used on different clock cycles
This sharing can help reduce the amount of hardware required.
  A single memory unit is used for both instructions and data.
  There is a single ALU, rather than an ALU and two adders.
  One or more registers are added after every major functional unit to hold the output of that unit until the value is used in a subsequent clock cycle.

## Slide 17: Pipeline
In next section, we’ll look at another implementation technique, called pipelining,
that uses a datapath very similar to the single-cycle datapath but is much more efficient by having a much higher throughput.
Pipelining improves efficiency by executing multiple instructions simultaneously.