## Slide 1: Pipelines
An overview of pipelining
Single-Cycle versus Pipelined Performance
Pipeline Hazards
Pipelined Datapath and Control.
Datapath walkthrough
Hazards solution
Textbook: P&H. Chapter 4.5.

## Slide 2: Laundry example
Ann, Brian, Cathy, Dave each have one load of clothes to wash, dry, fold, and put away
  Washer takes 30 minutes
  Dryer takes 30 minutes
  “Folder” takes 30 minutes
  “Stasher” takes 30 minutes to put clothes into drawers
A
B
C
D

## Slide 3: Sequential Laundry
Sequential laundry takes 8 hours for 4 loads
T
a
s
k
O
r
d
e
r
B
C
D
A
30
Time
30
30
30
30
30
30
30
30
30
30
30
30
30
30
30
6 PM
7
8
9
10
11
12
1
2 AM

## Slide 4: Pipelined Laundry
Pipelined laundry takes 3.5 hours for 4 loads!
T
a
s
k
O
r
d
e
r
B
C
D
A
12
2 AM
6 PM
7
8
9
10
11
1
Time
30
30
30
30
30
30
30

## Slide 5: Pipelining (1/2)
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Multiple tasks operating simultaneously using different resources
Potential speedup = Number pipe stages
Time to “fill” pipeline and time to “drain” it reduces speedup: 2.3X v. 4X in this example
6 PM
7
8
9
Time
B
C
D
A
30
30
30
30
30
30
30
T
a
s
k
O
r
d
e
r

## Slide 6: Pipelining (2/2)
Suppose new Washer takes 20 minutes, new Stasher takes 20 minutes. How much faster is pipeline?
Pipeline rate limited by slowest pipeline stage
Unbalanced lengths of pipe stages reduces speedup
6 PM
7
8
9
Time
B
C
D
A
30
30
30
30
30
30
30
T
a
s
k
O
r
d
e
r

## Slide 7: Steps in Executing MIPS
1) IFtch: Instruction Fetch, Increment PC
2) Dcd: Instruction Decode, Read Registers
3) Exec: Mem-ref: Calculate Address Arith-log: Perform Operation
4) Mem: Load: Read Data from Memory Store: Write Data to Memory
5) WB: Write Data Back to Register

## Slide 8: Single Cycle Datapath
PC
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write Back

## Slide 9: Pipeline registers
PC
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write Back
Need registers between stages
  To hold information produced in previous cycle

## Slide 10: More Detailed Pipeline

## Slide 11: IF for Load, Store, …

## Slide 12: ID for Load, Store, …

## Slide 13: EX for Load

## Slide 14: MEM for Load

## Slide 15: WB for Load – Oops!
Wrong register number

## Slide 16: Corrected Datapath for Load