## Slide 1: Pipelined Execution Representation
Every instruction must take same number of steps
  also called pipeline “stages”
  some instructions (shorter) will go idle in some stages
IFtch
Dcd
Exec
Mem
WB
IFtch
Dcd
Exec
Mem
WB
IFtch
Dcd
Exec
Mem
WB
IFtch
Dcd
Exec
Mem
WB
IFtch
Dcd
Exec
Mem
WB
IFtch
Dcd
Exec
Mem
WB
Time
5 stage pipeline => 5 instructions executing simultaneously, one at each pipeline stage

## Slide 2: Graphical Pipeline Diagrams
PC
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write Back
Use datapath figure below to represent pipeline
IFtch
Dcd
Exec
Mem
WB
ALU
I$
Reg
D$
Reg

## Slide 3: Graphical Pipeline Representation
I$
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 4: Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
What is pipelined clock rate?
  Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 5: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)

## Slide 6: Pipeline Speedup
If all stages are balanced
  i.e., all take the same time
Time between instructionspipelined = Time between instructionsnonpipelined Number of stages
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease

## Slide 7: Hazards
Situations that prevent starting the next logical instruction in the next clock cycle
Structural hazards
  Required resource is busy (e.g., roommate studying)
Data hazard
  Need to wait for previous instruction to complete its data read/write (e.g., pair of socks in different loads)
Control hazard
  Deciding on control action depends on previous instruction (e.g., how much detergent based on how clean prior load turns out)

## Slide 8: 1. Structural Hazard #1: Single Memory
Read same memory twice in same clock cycle
Conflict for use of a resource
I$
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load/Store requires memory access for data
Instruction fetch would have to stall for that cycle
  Causes a pipeline “bubble”
Solution, provide separate cache for I$ and for D$

## Slide 9: 1. Structural Hazard #2: Registers (1/2)
Can we read and write to registers simultaneously?
I$
Lw
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 10: 1. Structural Hazard #2: Registers (2/2)
Two different solutions have been used:
  1) RegFile access is VERY fast: takes less than half the time of ALU stage
    Write to Registers during first half of each clock cycle
    Read from Registers during second half of each clock cycle
  2) Build RegFile with independent read and write ports
Result: can perform Read and Write during same clock cycle

## Slide 11: Write /Read Registers in single cycle
I
n
s
t
r.
O
r
d
e
r
Load
Add
Store
Sub
Or
I$
Time (clock cycles)
I$
ALU
Reg
Reg
I$
D$
ALU
ALU
Reg
D$
Reg
I$
D$
Reg
ALU
Reg
Reg
Reg
D$
Reg
D$
ALU
(In Reg, right half highlight read, left half write)
Reg
I$

## Slide 12: Data Hazards (1/2)
Consider the following sequence of instructions
add $t0, $t1, $t2
sub $t4, $t0 ,$t3
and $t5, $t0 ,$t6
or $t7, $t0 ,$t8
xor $t9, $t0 ,$t10

## Slide 13: Data Hazards (2/2)
Data-flow backward in time are hazards
sub $t4,$t0,$t3
ALU
I$
Reg
D$
Reg
and $t5,$t0,$t6
ALU
I$
Reg
D$
Reg
or $t7,$t0,$t8
I$
ALU
Reg
D$
Reg
xor $t9,$t0,$t10
ALU
I$
Reg
D$
Reg
add $t0,$t1,$t2
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 14: Data Hazard Solution: Forwarding
Forward result from one stage to another
sub $t4,$t0,$t3
ALU
I$
Reg
D$
Reg
and $t5,$t0,$t6
ALU
I$
Reg
D$
Reg
or $t7,$t0,$t8
I$
ALU
Reg
D$
Reg
xor $t9,$t0,$t10
ALU
I$
Reg
D$
Reg
add $t0,$t1,$t2
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg
“or” hazard solved by register hardware

## Slide 15: Data Hazard: Load/Use (1/4)
Dataflow backwards in time are hazards
Can’t solve all cases with forwarding
Must stall instruction dependent on load, then forward (more hardware)
sub $t3,$t0,$t2
ALU
I$
Reg
D$
Reg
lw $t0,0($t1)
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg

## Slide 16: Data Hazard: Load/Use (2/4)
Hardware stalls pipeline (Called “interlock”)
sub $t3,$t0,$t2
ALU
I$
Reg
D$
Reg
bubble
and $t5,$t0,$t4
ALU
I$
Reg
D$
Reg
bubble
or $t7,$t0,$t6
I$
ALU
Reg
D$
bubble
lw $t0, 0($t1)
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg
Not in MIPS: (MIPS = Microprocessor without Interlocked Pipeline Stages)

## Slide 17: Data Hazard: Load/Use (3/4)
Instruction slot after a load is called “load delay slot”
If that instruction uses the result of the load, then the hardware interlock will stall it for one cycle.
Alternative: If the compiler puts an unrelated instruction in that slot, then no stall
Letting the hardware stall the instruction in the delay slot is equivalent to putting a nop in the slot (except the latter uses more code space)

## Slide 18: Data Hazard: Load/Use (4/4)
Stall is equivalent to nop
sub $t3,$t0,$t2
and $t5,$t0,$t4
or $t7,$t0,$t6
I$
ALU
Reg
D$
lw $t0, 0($t1)
ALU
I$
Reg
D$
Reg
bubble
bubble
bubble
bubble
bubble
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
nop

## Slide 19: Data Hazards: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction
C code for A = B + E; C = B + F;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
11 cycles
13 cycles

## Slide 20: 3. Control Hazards
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch

## Slide 21: Stall => 2 Bubbles/Clocks
Where do we do the compare for the branch?
I$
beq
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Solution Option 1: Stall on every branch until have new PC value
Would add 2 bubbles/clock cycles for every Branch! (~ 20% of instructions executed)

## Slide 22: Control Hazard: Branching
Optimization #1:
  Insert special branch comparator in Stage 2
  As soon as instruction is decoded (Opcode identifies it as a branch), immediately make a decision and set the new value of the PC
  Benefit: since branch is complete in Stage 2, only one unnecessary instruction is fetched
  Side Note: means that branches are idle in Stages 3, 4 and 5

## Slide 23: One Clock Cycle Stall
Branch comparator moved to Decode stage.
I$
beq
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 24: Control Hazards: Branching
Option 2: Predict outcome of a branch, fix up if guess wrong
  Must cancel all instructions in pipeline that depended on guess that was wrong
  This is called “flushing” the pipeline
Simplest hardware if we predict that all branches are NOT taken

## Slide 25: Control Hazards: Branching
Option #3: Redefine branches
  Old definition: if we take the branch, none of the instructions after the branch get executed by accident
  New definition: whether or not we take the branch, the single instruction immediately following the branch gets executed (the branch-delay slot)
Delayed Branch means we always execute inst after branch
This optimization is used with MIPS

## Slide 26: Example: Nondelayed vs. Delayed Branch
add $1, $2, $3
sub $4, $5, $6
beq $1, $4, Exit
or $8, $9, $10
xor $10, $1, $11
Nondelayed Branch
add $1, $2,$3
sub $4, $5, $6
beq $1, $4, Exit
or $8, $9, $10
xor $10, $1, $11
Delayed Branch
Exit:
Exit:

## Slide 27: Branch delay slot filling
Notes on Branch-Delay Slot
  Worst-Case Scenario: put a no-op in the branch-delay slot
  Better Case: place some instruction preceding the branch in the branch-delay slot—as long as the change doesn’t affect the logic of program
    Re-ordering instructions is common way to speed up programs
    Compiler usually finds such an instruction 50% of time
    Jumps also have a delay slot …